## Slide 1: Project – Smartphone Trucker Tracker
Project Presentation Adam Coetzee - 29982995

## Slide 2: Background – Trucking Industry
Trucking is essential for the economy
Fleets carry cargo over far distances
Misbehaving truckers are detrimental:
  Excessive stopping
  Unsafe driving
Managers can’t monitor them
A means of tracking is required

## Slide 3: What and how to track?
Acceleration
  Rapid acceleration/braking
Altitude
  Optimization analysis
Location
  Correct locations
  Taking optimal routes
Speed
  Obeying traffic laws
  Driving optimal speeds
Typically included in sensor suites of IoT devices
  Accelerometer, gyroscopes, magnetometers GPS units

## Slide 4: Problem Statement
Synthesize a tracking system for companies to track Acceleration, Altitude, Location and Speed captured with an IoT device
Continuously (or periodically) upload data to a central storage location
Provide an interface for managers to access this data, in a processed form which can be easily interpreted.

## Slide 5: Hypothesis
On-board smartphone sensors
I/O server receives log data from multiple devices
Data stored in Data Store
Web server performs back-end logic serving web pages to web application
Front end of web application renders web pages to manager
Objective:
Use logged data to generate detailed reports conveying useful information to managers
Benefit:
Managers can ensure efficient and proper operation

## Slide 6: Requirements
Smartphone Application
Identity Control
Log Acceleration, Altitude, Location and Speed every 2 minutes
Upload log data: Continuously or on request
Store log data locally until it can be transmitted
Log in the background
I/O Server
Connection must be secure
Multiple simultaneously connect
Identity verification and control
Transmit log data into the central database
Data Store
High performance data storage
Web Application
Support multiple managers and truckers
Generate detailed trip information about each trucker:
  Start/Stop Locations with corresponding times
  Delay between trips
  Display acceleration, altitude & location data for analysis

## Slide 7: Design – Methodolgy and System Context
C4 model for software design
System context defines high-level simple overview
System lifecycle

## Slide 8: Design - Contained subsystems and technologies
Expanding system context
Android Application
  Higher market share
  Kotlin provides less verbose code
  4.4 covers 99.6% of devices
MySQL
I/O Server
  C++ fast and efficient
  asio: asynchronous I/O
Web application
  ASP.NET
  C# backend
  HTML/CSS/JS frontend

## Slide 9: Design – Android Application
Model-View-ViewModel (MVVM)
Main Repository (Singleton): I/O operation calls
Tracking Service (Service Scoped) polls on-board sensors
SharedPreferences: Disk key-value preferences
ORM/Database: SQLite for storing cached log data
Server connector: Implements JSON over SSL protocol for communication

## Slide 10: Design – I/O Server
Server class listens for incoming connections
Each connection is assigned a Session which handles SSL implementation, including SSL handshake, sending/receiving messages
Request Handler serializes/deserializes JSON payload and handles business logic for handling request
MySQL Connector handles data access

## Slide 11: Design – JSON over SSL protocol
Between I/O server and Android Application
Communication is wrapped in a text-based JSON structure
Request payload
  Trucker ID
  Request Code
  Data payload
Response Payload
  Response Code
  Accompanying data (optional)

## Slide 12: Design – Web Application
MVC architecture
Views for the required displays
Models for conveying data
Controller returns specific models to views upon request
GoogleMaps API for visual map

## Slide 13: Design – Data Model

## Slide 14: Design – Data Processing
Goal: group GPS data into segments for each trip
Aggregate nearby logs
  not helpful to look at location logs very close in distance
  use some significant minimum threshold distance
Grouping aggregated logs into seperate trips
  Time difference between aggregated logs
  if large => trucker probably stopped => trip is complete

## Slide 15: Design – User Interface
Goals:
  Dynamic: Adjusting to different screen sizes
  Intuitive: Make the layout as obvious as possible
Android Application
  XML
  Constraint Layout: constraining elements to corners/edges of elements
Web application
  HTML div containers
  grid layout
  CSS with Bootstrap

## Slide 16: Development and Implementation
Git
Android Studio with Gradle
GCC
Dotnet SDK in Visual Studio Code
Incremental development and testing (git branches)

## Slide 17: Implementation – Android Application
Idle: Not running
Running: Foreground process polling sensors
Background: Displays notification
Logs are locally stashed
Acceleration is logged only with linear accelerometer (using sensor fusion)

## Slide 18: Implementation – I/O Server
Requests
  Update ID
  Verify ID
  Update Logs
Responses
  Fail
  OK
  Invalid Credentials
  DB Conn Failed
  Parse Fail

## Slide 19: Implementation – Web Application

## Slide 20: Implementation – Web Application

## Slide 21: Deployment
Daemons (web app and I/O server) deployed to a Linux VPS on the web
I/O server: Docker containers stable deployment environment
SystemD init system to run web application

## Slide 22: System Evaluation - Testing
4 devices tested
Occasional spikes in location (up to 300m)
Corrected in algorithm 1

## Slide 23: System Evaluation – Location Tracking
Trip to the shop
1st Trip: Fast and erratic
2nd Trip: Slow and steady

## Slide 24: System Evaluation – Speed Tracking

## Slide 25: System Evaluation – Acceleration Tracking
Erratic driving:
  Steep spikes in acceleration
  Higher maxima
Passive driving
  smoother spikes
  Lower maxima

## Slide 26: System Evaluation – Altitude Tracking

## Slide 27: System Evaluation – Android Application
Light on system resources
Data usage must be considered
Good performance on Android 10
Potential issues for other versions

## Slide 28: System Evaluation – I/O Server and Web Application
100% uptime: I/O server & Web application
  adequate exception handling

## Slide 29: Conclusion
Meets objectives and requirements
  Android app logs in the background and caches until transmission is possible
  I/O server relays data to database
  Web Application displays per-trip data
Usability
  Android application requires diligent use
  Better on new Android versions
  Samsung Galaxy A3 reasonable performance at R1400
  Multipurpose capabilities
Future Improvements
  External sensor integration via CAN bus
  Robustness: use of Android init systems etc
  Serialization Protocol: minimize data usage
  Sensor fusion: Improve sensor readings
  Acceleration data should be logged more often