## Slide 1: Project – Smartphone Trucker Tracker
Problem Contextualization Adam Coetzee - 29982995

## Slide 2: What is Fleet Tracker? Why is it important?
A full-stack live tracking solution using Android devices to track Truckers in a fleet
Provides managers of trucking companies a means to ensure truckers are
  driving to the correct location
  not stopping for excessive amounts of time
  driving appropriately, in a steady manner at adequate speeds
Tracks acceleration, altitude, location and speed
Such information allows managers to ensure efficiency

## Slide 3: Background – Trucking Industry
Trucking is essential for the economy
Fleets carry cargo over far distances
Misbehaving truckers are detrimental:
  Excessive stop times
  Unsafe driving
Managers can’t monitor them
A means of tracking is required

## Slide 4: What to track?
Acceleration
  Rapid acceleration/braking
Altitude
  Optimization analysis
Location
  Correct locations
  Taking optimal routes
Speed
  Obeying traffic laws
  Driving optimal speeds

## Slide 5: How to track? - Sensors
Acceleration
  Accelerometers provide raw data with gravity
  High pass filtering to remove gravity bias
  Sensor fusion: gyroscopes/magnetometers can clear gravity bias
Altitude
  GPS
Location
  GPS
Speed
  On-board vehicle speedometer
  Location delta
IoT devices come with sensor suites

## Slide 6: Problem Statement
Synthesize a tracking system for companies to track Acceleration, Altitude, Location and Speed captured with an IoT device
Continuously (or periodically) upload data to a central storage location
Provide an interface for managers to access this data, in a processed form which can be easily interpreted.

## Slide 7: Hypothesis
On-board smartphone sensors
I/O server receives log data from multiple devices
Data stored in Data Store
Web server performs back-end logic serving web pages to web application
Front end of web application renders web pages to manager
Objective:
Use logged data to generate detailed reports conveying useful information to managers
Benefit:
Managers can ensure efficient and proper operation

## Slide 8: Requirements
Smartphone Application
Identity Control
Log Acceleration, Altitude, Location and Speed every 2 minutes
Upload log data: Continuously or on request
Store log data locally until it can be transmitted to central store
Logging must take place in the background
I/O Server
Allow multiple Smartphone devices to simultaneously connect
Identity verification and control
Transmit log data into the central database
Data Store
High performance data storage
Web Application
Support multiple managers and truckers
Generate detailed trip information about each trucker:
  Start/Stop Locations with corresponding times
  Delay between trips
  Display acceleration, altitude & location data for analysis

## Slide 9: Literature Review

## Slide 10: System components

## Slide 11: Technologies

## Slide 12: Conclusion
System deployed (and tested) to a Linux VPS in docker containers
The required variables are logged (location accurate to 20m)
I/O server and web application maintain indefinite up-time (100%)
More testing required on Android Application, but runs well on Android 10
Further improvements to robustness and up-time can make this solution more reliable
Future expansion could include:
  Added integration with on-board vehicle sensors
  Improved algorithms and data processing for more accurate readings
Appealling solution for companies who want to use multipurpose devices, with cost-saving potential

## Slide 13: Smartphone Application
To be used by truckers
Log sensor data every 2 minutes
Send data to online server
Not responsible for generating reports

## Slide 14: I/O Server
High speed interface between smartphone application and data store
Capable of handling many requests
Only meant for data transfer

## Slide 15: Data Store
Storage Structure for trucking logs
Should be suited for many records
Compatiblity with system components

## Slide 16: Web Server
Data store access
Data processing – generate daily reports:
  locations travelled to
  Transit Times
  Stopping times
  Speed etc.
Server requests to web application

## Slide 17: Web Application
User Interface
Access reports about truckers

## Slide 18: Conclusion
Deliverables
  Smartphone Application
  Web Application
  Necessary supporting backend
Benefits
  Improved monitoring
  Potential optimization